## Slide 1: TECHNICAL & SAFETY COMMITTEE
International Parachuting Commission
FAI

## Slide 2: 2012 Safety Report
37 countries supplied data
5,230,563 skydives were made by
1,059,937 jumpers
53 people were killed skydiving
(these figures include Tandems)
1 Fatality per
98,690 jumps
19,999jumpers

## Slide 3: 53 Fatalities
11 Students (20%) 0-25 Freefalls
11 Intermed. (20%) 26-250 Freefalls
31 Experts (60%) 251 + Freefalls
Total 53
Cutaway & Low/No reserve pull 7
No pull/low pull on main 5
Others 41
Total 53

## Slide 4: ‘Other’ Fatalities (41)
Fast Canopies 10
Other Landing Errors 6
Equipment Problems 3
Tandem Fatalities 3
Unexplained jumper incapacity, main deployed, no input 2
Medical Conditions 2
Main malfunction, no action, spiralled to ground 2
Cutaway handle pulled, main released, no reserve pull 1
Main/reserve entanglement, after AAD fire at fast landing 1
Main/reserve entanglement after cutaway, 3-ring trapped 1
AFF Jump, student limp in harness at 300m 1
Collision with aircraft 1
Main cutaway by student at 50m, too low for reserve 1
Fast spirals to ground, jumper may have been incapacitated 1
Flag jump, flag escaped and obscured handles, no pull 1
Reserve opened incorrectly due to unstable position 1
Landed in tree, killed during rescue 1
Drowning 1
Freefall collision 1
Main canopy malfunction on landing 1
Total 41

## Slide 5: Fatalities – Largest Groups
1 Fast Canopies 10 – 19% of 53
2 Landing Errors 6 – 11% of 53
3 No or Low Main Canopy Activation 5 – 9% of 53
No or Low Cutaway & Reserve Activ. 5 – 9% of 53

## Slide 6: Significant Figures
  39 of the 53 fatalities (74%) appear to have occurred with the parachutist having at least one good parachute on his/her back
  22 of the 53 fatalities (42%) occurred after the successful deployment of the main parachute
  10 of the 53 fatalities (19%) might have been avoided by AAD use
  39 of the 53 fatalities (7%) appear to have been caused by human error4
5 (9.4%) of the 53 Fatalities were First Jump Students
3 ( 5.7%) of the 53 Fatalities were Tandem fatalities

## Slide 7: Some Trends & Issues
There was a very wide range of causes of fatalities in 2012, but the underlying factor appears to have been non-adherence to standard and fundamental practices.
High numbers of fatalities, 19 – 36%, resulting from canopy handling and landing issues – a continuing concern.

## Slide 8: Tandem - Solo
4,276,101 Solo jumps – 954,462 Tandems
Tandems 18.2% of all jumps, Tandem + Solo jumps
Tandems ratio to Solo Jumps - 22.3%
The ratio of Tandem to all jumps and to solo jumps is steadily increasing since 2005
Tandem Fatalities 3 (5.7%) Solo Fatalities 50 (94.3%)

## Slide 9
DISTRIBUTION OF REPORTS
This Power Point presentation and the full 2012 Safety Report, have been sent by e-mail to all respondents and to all other countries for which there are e-mail addresses.
CDs are available to IPC Delegates and to those who request copies.
The CD has the following material -
2012 Safety Report 2012 Safety Report Power Point Presentation
Safety Survey 2013 Form Safety Survey 2013 Notes
Information Notices (5) issued in 2013 by T & S Committee
APPEAL
Those countries who did not report for 2012 are requested to make a special effort to do so for 2013. The compilation of data is to the benefit of the country gathering same, and to
the worldwide skydiving community.
Distribution of Reports