## Slide 1
International Parachuting Commission
FAI
Notes: <number>

## Slide 2
37 countries responded, from a possible approximately 85, a response rate of 44%.
The response rate was similar to previous years and has been about this rate for the 27 years of the Safety Survey.
Once again countries are encouraged to put in place systems for the collection of the type of data in this report.
Such data is invaluable - for use by parachuting organisations, dropzones, those involved in the areas of technical and safety matters, and when dealing with authorities.

## Slide 3: 2014 Safety Report
37 countries supplied data
6,237,725 skydives were made by
1,314,867 jumpers
31 people were killed skydiving
(these figures include Tandems; there were three Tandem fatalities in 2014)
1 Fatality per
201,207 Jumps
42,415 Jumpers

## Slide 4: 31 Fatalities
3 Students (10%) 0-25 Freefalls
7 Intermediate (23%) 26-250 Freefalls
21 Experts (68%) 251 + Freefalls
Total 31
Cutaway & Low/No reserve pull 4
No pull/low pull on main 2
Others 25
Total 31

## Slide 5: ‘Other’ Fatalities (25)
Fast Canopies - Intentional Fast Landings 6
Equipment Related Issues 4
Canopy Collision 4
Tandem Fatalities 3
Freefall Collision 2
Incorrect Emergency procedures 1
Reserve bridle entanglement with camera
helmet after unstable reserve activation 1
Medical Issue 1
Main malfunction, no action 1
Low radical turn, high impact with water,
causing lung damage and death 1
Instability, no Main deployment, AAD activated
reserve, freebag caught on jumper, insufficient
height for reserve deployment, reserve lines
trapped under jumper’s arm 1
Total 25

## Slide 6: Fatalities – Largest Groups
1 Fast Canopies 6 - 19% of 31
2 Equipment relates issues
and Canopy Collision – each at 4 – 13% of 31
3 Tandem Fatalities 3 – 10% of 31
Canopy handling issues, combined –
12 (39% of total fatalities, 31)

## Slide 7: Significant Figures
  OF THE 31 FATALITIES
  20 (65%) appear to have occurred with the parachutist having at least one good parachute on his/her back
  11 (35%) occurred after the successful deployment of the main parachute
  5 (16%) might have been avoided by AAD use
  23 (74%) appear to have been caused by human error
None of the 2014 Fatalities were First Jump Students

## Slide 8: Some Trends & Issues
Continuing high percentage of fatalities, 12 (39% of 31) resulting from canopy handling, canopy control, and landing issues.
Roughly similar percentage distribution of fatalities between Student/Intermediate/Expert as in previous years . The category ‘Expert Skydiver’ continues to have the most fatalities, but it has the biggest numbers of jumps.
AAD and RSL are both now widely used.

## Slide 9: Tandem - Solo
Tandems 19% of all jumps, Tandem + Solo
5,075,020 Solo jumps – 1,162,705 Tandems
Tandem Fatalities 3 ; Solo Fatalities 28 (31 total)

## Slide 10
This report, along with this and Power Point presentation, has been sent by
e-mail to all respondents and to all other countries for which the
T&S Committee has e-mail addresses.
CDs are available to IPC Delegates and to Technical and Safety Officers
who request copies.
Distribution of Reports
The CD has the following material -
2014 Safety Survey Report
2014 Safety Survey Report Power Point Presentation
Safety Survey 2015 Form
Safety Survey 2015 Notes
Information Notices (3) issued in 2015 by the IPC’s Technical & Safety Committee
APPEAL
Those countries who did not report for 2014 are requested to make a special
effort to do so for 2015. The compilation of data is to the benefit of the country gathering same, and to the worldwide skydiving community.
Distribution of Reports