## Slide 1
International Parachuting Commission
FAI
Notes: <number>

## Slide 2
37 countries responded, from a possible approximately 85, a response rate of 44%.
The response rate was similar to previous years and has been about this rate for the 28 years of the Safety Survey.
Once again countries are encouraged to put in place systems for the collection of the type of data in this report.
Such data is invaluable - for use by parachuting organisations, dropzones, those involved in the areas of technical and safety matters, and when dealing with authorities.

## Slide 3: 2015 Safety Report
37 countries supplied data
6,627,023 skydives were made by
1,325,838 jumpers
60 people were killed skydiving
(these figures include Tandems; there was one
Tandem fatalitiy in 2015)
1 Fatality per
110,450 Jumps
22,097 Jumpers

## Slide 4: 60 Fatalities
11 Students (18%) 0-25 Freefalls
11 Intermediate (18%) 26-250 Freefalls
38 Experts (63%) 251 + Freefalls
Total 60
Cutaway & Low/No Reserve pull 7
No pull/low pull on main 3
Others 50
Total 60

## Slide 5: ‘Other’ Fatalities (50)
Fast Canopies - Intentional Fast Landings 12
Other Landing Errors 7
Equipment Related Issues 6
Canopy Collision 5
Main/Reserve Entanglement 3
Incorrect Emergency Procedures 3
Main Malfunction, no action 3
Tandem Fatality 1
Freefall Collision 1
No pull, AAD fired and cut loop but no reserve deployment 1
Foot caught on line, cut away, reserve partly opened 1
Spinning main, reserve deployed 800 ft., no cutaway 1
Medical Issue 1
Apparent incapacitation 1
Canopy deflated at low altitude, structural failure 1
Collision with aircraft – jumper over runway 1
Turbulence at low altitude 1
Wingsuit - one wing not closed, vertical descent rate too low 1
to fire AAD
Total 50

## Slide 6: Fatalities – Largest Groups
1 Fast Canopies 12 - 20% of 60
2 Other Landing Errors 7 – 12% of 60
3 Equipment Related issues 6 – 10% of 60
Canopy handling issues, combined –
19 (32% of total fatalities, 60)

## Slide 7: Significant Figures
  OF THE 60 FATALITIES
  41 (68%) appear to have occurred with the parachutist having at least one good parachute on his/her back
  29 (48%) occurred after the successful deployment of the main parachute
  6 (10%) might have been avoided by AAD use
  42 (70%) appear to have been caused by human error
Five of the 2015 fatalities were First Jump Students

## Slide 8: Some Trends & Issues
Continuing high percentage of fatalities, 19 (32% of 60) resulting from canopy handling, canopy control, and landing issues.
Roughly similar percentage distribution of fatalities between Student/Intermediate/Expert as in previous years . The category ‘Expert Skydiver’ continues to have the most fatalities, but it has the biggest numbers of jumps.
AAD and RSL are both now widely used.

## Slide 9: Tandem - Solo
Tandems 17.6% of all jumps, Tandem + Solo
5,455,873 Solo jumps – 1,171, 150 Tandems
Tandem Fatalities 1; Solo Fatalities 59 (60 total)

## Slide 10
This report, along with this and Power Point presentation, has been sent by
e-mail to all respondents and to all other countries for which the
T&S Committee has e-mail addresses.
CDs are available to IPC Delegates and to Technical and Safety Officers
who request copies.
The CD has the following material -
2015 Safety Survey Report
2015 Safety Survey Report Power Point Presentation
Safety Survey 2016 Form
Safety Survey 2016 Notes
Information Notices (2) issued in 2016 by the IPC’s Technical & Safety Committee
Parachuting Aircraft Incidents/Accidents Report
APPEAL
Those countries who did not report for 2015 are requested to make a special
effort to do so for 2016. The compilation of data is to the benefit of the country gathering same, and to the worldwide skydiving community.
Distribution of Reports