## Slide 1: TECHNICAL & SAFETY COMMITTEE
International Parachuting Commission
FAI
Notes: <number>

## Slide 2: Responses
There was a sharp decline in the number of Safety Survey responses for 2011 with only 36 countries reporting.
This is very poor, given that -
Safety is one of the platforms of the IPC Strategic Plan.
60 countries registered to compete at Mondial 2012.
It may be the case that Safety Data Collection is not high on the priority list, even for some countries in which sport parachuting is highly or moderately well developed.
It would appear somewhat strange that countries would not have data collection as part of the function of their National Parachute Federation, to have figures to present when seeking state funding or sponsorship,
or when liaising with their Aviation Authorities and discussing activity and incidents.

## Slide 3: 2011 Safety Report
36 countries supplied data
6,079,723 skydives were made by
1,122,022 jumpers
52 people were killed skydiving
(these figures include Tandems)
1 Fatality per
116,918 jumps
21,577jumpers

## Slide 4: 52 Fatalities
10 Students (19%) 0-25 Freefalls
7 Intermed. (13%) 26-250 Freefalls
35 Experts (67%) 251 + Freefalls
Total 52
Cutaway & Low/No reserve pull 1
No pull/low pull on main 7
Others 44
Total 52

## Slide 5: ‘Other’ Fatalities (44)
Fast Canopies - Intentional Fast Landings 15
Canopy Collisions/Entanglements 11
Landing Errors 6
Equipment Problems 5
Tandem Fatalities 2
Main Malfunction – No Cutaway 2
Freefall Collision 1
Main /Reserve Entanglement 1
Main Mal/ No Reserve Pull/AAD fired
but reserve not inflated in time 1
Total 44

## Slide 6: Fatalities – Largest Groups
1 Fast Canopies 15 - 29% of 52
2 Canopy Collisions
Entanglements after opening 11 - 21% of 52
3 No or low Main Activation 7 – 13% of 52

## Slide 7: Significant Figures
  44 of the 52 fatalities (85%) appear to have occurred with the parachutist having at least one good parachute on his/her back
  32 of the 52 fatalities (62%) occurred after the successful deployment of the main parachute
  9 of the 52 fatalities (17%) might have been avoided by AAD use
  45 of the 52 fatalities (87%) appear to have been caused by human error
None of the 2011 Fatalities were First Jump Students
2 (4%) of the 52 Fatalities were Tandem fatalities

## Slide 8: Some Trends & Issues
Increasing high percentage of fatalities, 62% (32) resulting from canopy handling, canopy control, and landing issues.
Roughly similar percentage distribution of fatalities between Student/Intermediate/Expert as in previous years – no significant change, allowing for the mix of responding countries. The category ‘Expert skydivers’ continues to have the most fatalities, but they have the biggest numbers of jumps.
Increased use of AAD and RSL reported

## Slide 9: Tandem - Solo
Tandems 16.3% of all jumps, Tandem + Solo jumps
2010 – 15.1%; 2009 – 13.5%; 2008 - 12.1%; 2007 - 9.6%; 2006 – 12.2%; 2005 – 10.4%
5,089,679 Solo jumps – 990,044Tandems
Tandem Fatalities 2 (4%); Solo Fatalities 50 (96%)

## Slide 10
DISTRIBUTION OF REPORTS
This report, along with this and Power Point presentation, has been sent by
e-mail to all respondents and to all other countries for which the
T&S Committee has e-mail addresses.
CDs are available to IPC Delegates and to Technical and Safety Officers
who request copies.
The CD has the following material -
2011 Safety Survey Report
2011 Safety Survey Report Power Point Presentation
Safety Survey 2012 Form
Safety Survey 2012 Notes
APPEAL
Those countries who did not report for 2011 are requested to make a special effort to do so for 2012. The compilation of data is to the benefit of the country gathering same, and tothe worldwide skydiving community.
Distribution of Reports